Telecommunications Exam Solutions

- Two hour Exam
- Answer 2 of 3 Questions
- 1 hour per question

2016 Exam:

Q1 (a) – Flow Control

I) Define the term ‘flow control’ and explain the trade-off in the design of flow control mechanisms by discussing a number of flow control mechanisms.

Flow Control is the method by which the amount of data transmitted to a receiver is controlled. It determines how packets are sent between two nodes within a telecommunication network and defies how errors should be handled.

1. Stop-And-Wait ARQ: This is when a sender waits to receive an ACK from the receiver before sending the next packet. Good because it ensures no packets are lost, however it is time consuming and isn’t very efficient.
2. Go-Back-N ARQ: This is when if an ACK for a specific frame has not been received within a given time frame the system re-sends all subsequent frames from the last ACK onwards. This is good because it allows transmission to continue, however all subsequent frames must be resent which is very ineffecient.
3. Selective Repeat ARQ: This is when a receiver keeps track of the frame it expects next, informing the sender also which frame it expects. If a receiver receives a packet that does not match the packet number it expected it returns an NAK informing the sender of which packet it is missing. This is good because it allows continuous transmission and it also enables individual packets to be resent rather than the entire transmission.

II) Assume that you are asked to provide a Selective Repeat mechanism and a Go-Back-N mechanism for communication between two stations A and B. Describe with the help of diagrams the exchange of 10 frames between A and B for both mechanisms.

Selective Repeat ARQ

- Frame 0 is the first packet sent between A and B.
- Frame 1 is then sent, receiver expected this frame, returns ACK2 (expects Frame 2 next)
- Frame 2 is lost, next frame received is Frame 3.
- This is the wrong frame so receiver returns NAK2 informing that it expected Frame 2.
- Frame 2 is resent.

Go-Back-N ARQ

- Frame 0 is sent, senders receives an ACK informing it that Frame 1 is expected next.
- Frame 1 is sent, but is lost. Transmission continues and no ACK is received within time period.
- Transmission is timed out. System goes back to last ACK and re-sends Frame 1.
- Transmission continues from here onwards and all subsequent are re-transmitted to receiver.

III) Discuss the advantages and disadvantages of a Selective Repeat Mechanism in comparison to a Stop-and-Wait mechanism.

By using a Selective Repeat Mechanism it enables you to fluidly transmit between a sender and a receiver whilst also handling any lost packets quite efficiently as only individual lost packets need to be resent.

In comparison, a Stop-and-Wait mechanism doesn’t allow for fluid transmission as the sender must halt transmission and wait to receive an ACK from the receiver before transmitting the next frame. This is not ideal in a real-life situation where transmission times may be long and transmissions may expensive.

Q1 (b) – Flow Control

I) Assume you have a connection that exhibits sporadic burst errors. Transmissions across the connection are not costly and the transmission delay is short. Propose an error detection approach and contrast it against alternatives.

Burst Errors are when errors are found to be spread across a wide range of bits and not just focused single bit errors.

As a result the entire information must be checked to ensure validity. To achieve this the desired error checking method would be Cyclic-Redundancy Check (CRC). This is achieved using what is called a Checksum value. The Checksum value is generated as a result of a defined polynomial which can be generated as follows.

The Cyclic-Redundancy Check (CRC) is done as follows.

CRC is the preferred method for sporadic burst errors as it ensure the validity of the entire data, whereas Checksum or Even Parity check only account for single bit errors.

ii) Assume you have a connection that exhibits few errors that are generally limited to single bits. Transmissions across the connection are costly and the transmission delay is long. Propose an error detection approach and contrast it against alternatives.

When checking for single bit errors you have two options:

- Even Parity Check
- Checksum

Since transmissions over the network are costly you would want to transmit as little information as possible. The more ideal method for this would be to use Even Parity Bit as it means only one extra bit of data is needed to be transferred per section ( the parity bit ). This results in a total data transfer of (k + 1) * b (k being sections, n being number of sections, b being bits per section).

Whereas for Checksum each section is added and then complemented and the resulting checksum is transferred. This results in a total data transfer of (k + k/n) * b (k being sections, n being number of sections, b being bits per section).

Q2 (a) – Medium Access Control

I) Assume that your wired network currently uses Time-Division Multiple Access (TDMA) to accommodate 6 stations. Explain how stations gain access to this medium and the advantages and disadvantages of this approach.

In Time-Division Multiple Access (TDMA) users are granted access to the full bandwidth of the network for 1/N of the time.

Access to the channel is in rounds. Each station gets a fixed length slot in each round. Unused slots go idle.

TMDA Advantages:

- Efficient use of frequency spectrum.
- Operational costs lower than FDMA.
- Suitable for various types of traffic (e.g voice, data, video)
- Resources used effectively, preserves battery life

TMDA Disadvantages:

Network and spectrum planning require more efforts.
- Multi path interference affects call quality.
- Switching between base station cells results in dropped calls.

II) Propose an alternative protocol to TDMA that would be suitable for a varying number of stations . Explain how stations would gain access to this protocol and discuss the advantages and disadvantages.

In Frequency-Division Multiple Access (FDMA) users are granted 1/N of the total bandwidth for an unlimited amount of time.

Channel spectrum is divided into various frequency bands depending on the number of users. Each station is assigned a fixed frequency band. Unused transmission time in frequency bands go idle.

FDMA Advantages:

- Separate bands for uplink and downlink.
- Stations can transmit and receive simultaneously.
- Very simple to implement with respect to hardware.
- Efficient when managing constant traffic.

FDMA Disadvantages:

Frequencies allocated permanently, waste of spectrum when idle.
- Network and spectrum planning is difficult.
- Guard bands to prevent interference, waste of resources.
- Requires RF filters, increasing costs.
- Maximum bit rate is constant, doesn’t suit varying data rates.
Q2 (b) – Medium Access Control

IEEE 802.11 defines two methods of medium access control, the Distributed Coordination Function (DCF) and the Point Coordination Function (PCF).

I) Describe the two methods DCF and PCF and discuss the importance of interframe spaces.

Distributed Coordination Function (DCF):

- This is when stations compete for access to the medium.
- First checks to ensure radio link is clear before transmission.
- If not idle, wait using exponential backoff
- Hidden station / Expose station problem.
- Used CSMA/CA (no collision avoidance).
- Uses DIFS (Distributed Interframe Spaces)

Point Coordination Function (DCF):

- This is when a point coordinator polls stations.
- Polls stations to see if they desire access to medium.
- Uses round-robin technique when Mpolling.
- Stations must respond within SIFS.
- Uses PIFS (Point Interframe Spaces).

Interframe Spaces

Interframe spaces define the minimum time between frames. They are important as they directly influence how long stations must wait before gaining access to a medium.

- Short IFS (SIFS): The minimum time between frames.
- Distributed IFS (DIFS): The minimum time between the end of a transmission and the start of the next transmission.
- Point IFS (PIFS): The minimum time before polling station will allow transmission of the next transmission.

SIFS < PIFS < DIFS

II) Explain the coordination of communication between an access point and 5 laptops when using DCF and PCF.

Distributed Coordination Function (DCF)

1. All stations wait DIFS + random backoff.
2. Station with least backoff attempts to gain access.
3. Someone succeeds and begins transmission (RTS – Right to Send).
4. Other nodes backoff exponentially.
5. Transmission finishes and medium is free for next transmission.

Point Coordination Function (PCF)

1. Wait SIFS, poll next station.
2. If ACK, allow to transmit, when finished wait PIFS.
3. Else poll next station.

Q2 (a) – Routing

Trinity College currently uses Class B network addresses within the range 134.226.0.0 to 134.226.255.255 for a number of its network node. The network has around 20,000 nodes. The traffic of 200 of these nodes is allowed to pass to the internet without being blocked by routers. The traffic of the remaining nodes is never directly routed into the internet.

I) Describe the routing of an IP packet from a node inside the network to a server outside the network, blocked & unblocked by routers.

Router Connection:

1. Laptop A sends IP packet to its connected router.
2. Connected router knows how to get to destination.
3. Router forwards packet to connected gateway/router.
4. Packet arrives at outer-network (74.125.0.0)
5. Packet is then routed throughout subnet-work until it arrives at destination.
6. Packet decoded at destination (Google – 74.125.24.104).

Non-Router Connection:

1. Laptop (node) is connected directly to the internet.
2. Laptop sends IP packet directly to ISP with a defined destination.
3. Packet does not need to go through a router as it is connected directly to the internet.
4. Packet traverses the internet.
5. Packet arrives at outer-network (74.125.0.0).
6. Packet is then routed throughout subnet-work until it arrives at destination.
7. Packet reaches destination node (Google – 74.125.24.104).
8. Packet decoded at destination.

I) Describe the routing of an IP packet from a node outside the network to a node inside the network, blocked & unblocked by routers.

Router Connection:

1. Google server at 74.125.24.105 would like to send packet to Trinity node (188.141.1.1)
2. Server sends IP packet to its connected router.
3. Router sends packet to the outer-network router (74.125.0.0).
4. Router then forwards packet to the respective gateway/router (next hop).
5. This is repeated until packet arrives at Trinity address (188.141.0.0).
6. Packet is then routed through sub-network until it arrives at 188.141.1.1.
7. Packet is decoded at node.

Non-Router Connection:

1. Google server is directly connected to the internet.
2. Packet does not need to be sent to outer-network, sent directly to next gateway.
3. Packet is routed throughout the internet.
4. Packet is then routed through sub-network until it arrives at 188.141.1.1.
5. Packet is decoded at node.

II) Describe the application of Network Address Translation (NAT) to the network of Trinity College , the possible allocation of addresses and the effect that this may have on the consumption of publicly routed IP addresses.

NAT Gateway translates traffic from the local network to the IP address of the gateway. This involves processing outgoing & incoming packets (translating addresses, re-calculating checksums etc). The Gateway maintains a table to match incoming and outgoing packets including ID’s for applications.

Within the Trinity college network Network Address Translation (NAT) may be used to direct traffic between the subnetworks within the college e.g SCSS and the other schools. Network Address Translation (NAT) may be used multiple times say in the following order:

Packet for SCSS Node (134.226.60.215)

1. Arrives out outer network NAT Gateway (134.226.0.0)
2. Routed to sub-network SCSS NAT Gateway (134.226.60.0)
3. SCSS NAT Gateway forwards packet directly to SCSS Node (134.226.60.215)

Q3 (b) – Routing

Link State Routing (LSR) represents one of the major routing concepts.

I) Describe the two components of LSR ie the establishing of a view of the topology and the execution of Dijkstra’s Shortest Path algorithm.

The first component of Link State Routing (LSR) is the establishment of a view of the topology. All nodes and routers within the network must share their information either to each other or to an external controller. The information they must share in order to allow for Dijkstra’s shortest path algorithm to be executed is:

- List of all connected nodes/routers
- Distance to all connected nodes/routers

Once this information has been shared it is then possible for Dijksta’s shortest path algorithm to be run. In short hand Dijkstra’s algorithm is executed as follows:

1. Choose a source node
2. Assign a cost of 0 to this node and make it the first permanent node
3. Examine each neighbor node of the last permanent node
4. Assign a cumulative cost to each node and make it tentative
5. Among the list of tentative nodes
   a) Find the node with the smallest cumulative cost and make it permanent

   b) If node can be reached from more than one direction choose the one with shortest	cumulative cost

Repeat steps 3 to 5 until every node becomes permanent.

I) Explain the process of establishing a routing table for node I using the two components with the help of the following diagram.

First of all, either an external controller or each node within the graph is informed of the connections to each other node and their respective distances.

1. Node I is selected as root node
2. Add Node I to Settled Nodes

Examine all nodes adjacent to Node I:

- Node E – 240
- Node F – 150
- Node J – 340
1. Add each of the nodes to Tentative Nodes
2. Select Node F and add to Settled Nodes

Examine all nodes adjacent to Node F:

- Node G – 160
- Node E – 180
- Node B – 120

Repeat steps until all nodes are settled.

   Routing Table	Tentative Nodes
I 0 -

   Routing Table	Tentative Nodes
I 0 -	E 240 I / F 150 I / J 340 I

   Routing Table	Tentative Nodes
I 0 - / F 150 I	E 240 I / F 150 I / J 340 I

   Routing Table	Tentative Nodes
I 0 - / F 150 I / E 240 I	E 240 I / J 340 I / G 150+160 F / B 150+120 F / E 150+180 F

   Routing Table	Tentative Nodes
I 0 - / F 150 I / E 240 I / B 270 E	J 340 I / G 150+160 F / B 150+120 F / A 150+180+140 E

   Routing Table	Tentative Nodes
I 0 - / F 150 I / E 240 I / B 270 E / G 310 F	J 340 I / G 150+160 F / A 240+140 E / C 270+410 B / D 270+170 B

   Routing Table	Tentative Nodes
I 0 - / F 150 I / E 240 I / B 270 E / G 310 F / J 340 I	J 340 I / A 240+140 E / C 270+410 B / D 270+170 B / J 310+90 G / D 310+230 G

   Routing Table	Tentative Nodes
I 0 - / F 150 I / E 240 I / B 270 E / G 310 F / J 340 I / A 380 E	A 240+140 E / C 270+410 B / D 270+170 B / H 340+210 J

   Routing Table	Tentative Nodes
I 0 - / F 150 I / E 240 I / B 270 E / G 310 F / J 340 I / A 380 E / D 440 B	C 270+410 B / D 270+170 B / H 340+210 J

   Routing Table	Tentative Nodes
I 0 - / F 150 I / E 240 I / B 270 E / G 310 F / J 340 I / A 380 E / D 440 B / H 550 J	C 270+410 B / H 340+210 J / C 440+160 D / H 440+140 D

   Routing Table	Tentative Nodes
I 0 - / F 150 I / E 240 I / B 270 E / G 310 F / J 340 I / A 380 E / D 440 B / H 550 J / C 600 D	C 270+410 B / C 440+160 D / C 550+290 H

**ALL NODES HAVE NOW BEEN SETTLED**